## Slide 1: The concept of Green chemical engineering
Fyodor Malchik

## Slide 2: Presentation Outline
Introduction to Green Engineering (GE) and Inherent Safety (IS)
  GE definition, concepts, principles, and tools
  IS concepts and tools
  Similarities and differences between GE and IS
Environmentally-Conscious Process Design Methodology
  A hierarchical approach with three “tiers” of impact assessment
  A case study for maleic anhydride (MA) process design
  Early design methods and software tools
  Flowsheet synthesis, assessment, and software tools
  Flowsheet optimization - comparison of process improvement
  Summary of environmentally-conscious design methods
Notes: This presentation is divided into two main parts. The first is an introduction to the concepts and tools of Green Engineering (GE) and of Inherent Safety (IS). Comparisons and differences between GE and IS will also be discussed. The second part describes in some detail a systematic and hierarchical framework for the design, assessment, and improvement of chemical processes using environmental impacts as design objectives.

## Slide 3: What is Green Engineering?
Design, commercialization and use of processes and products that are feasible and economical while minimizing:
+ Risk to human health and the environment
+ Generation of pollution at the source
Notes: This is a working definition of Green Engineering as given by the US EPA, Office of Pollution Prevention and Toxics. The key words to notice here are “risk to human health and the environment” and “feasible and economical”. In Green Engineering it is not sufficient to be only green, but other design considerations must also be included, like economics, safety, and others.

## Slide 4: Energy Use: U.S. Industry
Annual Energy Review 1997, U.S. DOE, Energy Information Administration, Washington, DC, DOE/EIA-0384(97)
SIC Code 1015 BTU/yr
29 Petroleum/Coal Products 6.34
28 Chemicals / Allied Products 5.33
26 Paper / Allied Products 2.67
33 Primary Metals Industries 2.46
20 Food / Kindred Products 1.19
32 Stone,Clay and Glass 0.94
24 Lumber / Wood Products 0.49
Numbers represent roughly the % of US annual energy consumption
Notes: Chemical Manufacturing, allied products, petroleum and coal products consume for about 12% of the annual US energy consumption. When paper products is added, about 14%.

## Slide 5: Pollution Prevention (P2) vs. Pollution Control (PC)
Chemical
Process
Raw Materials,
Energy
Products
Wastes
Pollution
Control
Modified
Chemical
Process
Raw Materials,
Energy
Products
Wastes
Pollution
Control
Recycle
Traditional Process
Greener Process
Higher income,
Higher operating costs
Lower PC costs
Notes: Green Engineering emphasizes pollution prevention and risk reduction over pollution control at the end of pipe. Pollution prevention can be accomplished through more efficient utilization of mass and energy, generation of fewer and less toxic pollutants, and reuse and recycle when pollutants are generated or when unconverted raw materials are present. Process modification to accomplish pollution prevention is one major approach in designing cleaner processes and in retrofitting existing processes. Pollution prevention can lead to higher production efficiencies and fewer wastes to treat using pollution control.

## Slide 6: Examples of Green Engineering
Chemical reactions using environmentally-benign solvents
Improved catalysts
  that increase selectivity and reduce wastes
  that improve product quality and reduce environmental impacts
  that process wastes into valuable products
Separations using supercritical CO2 rather than R-Cl solvents
Separative reactors that boost yield and selectivity
Fuel cells in transportation and electricity generation
CO2 sequestration
New designs that integrate mass and energy more efficiently
Process modifications that reduce emissions
Environmentally-conscious design methods and software tools.
Notes: Green Engineering has many aspects that link well with traditional chemical engineering specialties, such as reaction engineering, separations engineering, and process design. This list shows some current GE research areas within Chemical Engineering. Green Engineering for chemical engineers seeks to develop advances in chemical process technologies that result in lower environmental impacts while improving profitability.

## Slide 7: Environmentally-Conscious Design
Methods and tools to evaluate environmental consequences of chemical processes and products are needed.
  quantify multiple environmental impacts,
  guide process and product design activities
  improve environmental performance of chemical processes and products
Environmental impacts
  energy consumption - raw materials consumption
  impacts to air, water - solid wastes
  human health impacts - toxic effects to ecosystems
Economic Performance
  costs, profitability
Notes: Although Green Engineering involves advances in chemical process technologies, ultimately methods are needed to quantify improvements to the environment as a results of incorporating these technologies into chemical processes. Environmentally-conscious design methodologies are thus required to guide the design process and to provide indicators of environmental performance for decision-making.

## Slide 8: Tools of Environmentally-Conscious Chemical Process Design and Analysis
E-CD
Environmental Fate Properties
• databases
• estimation
Chemical Process Properties
• thermodynamics
• reactions
• transport
Chemical Process Models
• simulation
• waste generation and release
Environmental Fate Models
• single compartment
• multi-media
Environmental Impacts Models
• midpoint vs endpoint
• normalization
• valuation
Process Integration
• mass integration
• heat integration
Process Optimization
• multi-objective
• mixed integer
• non-linear
Hierarchical Design
Notes: Computer-aided tools for E-CD can help meet environmental challenges by putting in place environmental impact assessment methodologies and tools that inform decision-making and lead to pollution prevention and environmental risk reduction. These tools fit into several categories: Property estimation or databases, models for process and environmental performance, and process integration and optimization. These tools are being developed by industry, government, and academia.

## Slide 9: Principles of Green Engineering
The Sandestin Declaration on
Green Engineering Principles
Green Engineering transforms existing engineering disciplines and practices to those that lead to sustainability. Green Engineering incorporates development and implementation of products, processes, and systems that meet technical and cost objectives while protecting human health and welfare and elevates the protection of the biosphere as a criterion in engineering solutions.
Green Engineering: Defining the Principles, Engineering Conferences International, Sandestin, FL, USA, May 17-22, 2003.
Notes: A recent multi-disciplinary engineering conference was held to achieve a consensus on guiding principles for Green Engineering. There are many complimentary ideas in both this and the prior EPA definition.

## Slide 10: Principles of Green Engineering
The Sandestin GE Principles
Engineer processes and products holistically, use systems analysis, and integrate environmental impact assessment tools.
Conserve and improve natural ecosystems while protecting human health and well-being
Use life-cycle thinking in all engineering activities
Ensure that all material and energy inputs and outputs are as inherently safe and benign as possible
Minimize depletion of natural resources
Strive to prevent waste
Develop and apply engineering solutions, while being cognizant of local geography, aspirations, and cultures
Create engineering solutions beyond current or dominant technologies; improve, innovate and invent (technologies) to achieve sustainability
Actively engage communities and stakeholders in development of engineering solutions
Green Engineering: Defining the Principles, Engineering Conferences International, Sandestin, FL, USA, May 17-22, 2003.
Notes: Here are the 9 GE principles from the Sandenstin Conference. These guiding principles stress pollution prevention, life-cycle thinking, efficient utilization of resources as approaches in the design and development of technologies, as well as minmizing ecosystem impacts as design objectives.

## Slide 11: Definition of Inherent Safety (IS)
A chemical manufacturing process is described as inherently safer if it reduces or eliminates hazards associated with materials used and operations, and this reduction or elimination is a permanent and inseparable part of the process technology. (Kletz, 1991; Hendershot, 1997a, b)
Notes: The definition of Inherent Safety emphasizes hazards elimination and reduction, in much the same way that GE stresses risk reduction for human health effects and for the environment. The approach is much the same, yet the targets are different. In IS, the target is protection of workers at the facility while GE targets the protection of the environment and general population.

## Slide 12: IS Concepts
Intensification - using less of a hazardous material
Example: improved catalysts can reduce the size of equipment and minimize consequences of accidents.
Attenuation - using a hazardous material in a less hazardous form. Example: larger size of particle for flammable dust or a diluted form of hazardous material like aqueous acid rather than anhydrous acid.
Substitution - using a safer material or production of a safer product. Example: substituting water for a flammable solvent in latex paints compared to oil base paints.
Notes: This slide and the next show the main concepts of IS.

## Slide 13: IS Concepts (cont.)
limitation - minimizing the effect of an incident. Example: smaller diameter of pipe for transport of toxic gases and liquids will minimize the dispersion of the material when an accident does occur
Simplification - reducing the opportunities for error and malfunction. Example: easier-to-understand instructions to operators.

## Slide 14: Comparison between IS and (GE)
Strategy/Tenet (Based on IS) | Example Concepts | Inherent Safety (IS) | Green Engineering (GE)
Substitution | Reaction chemistry, Feedstocks, Catalysts, Solvents, Fuel selection | √√√√ | √√√√
Minimization | Process Intensification, Recycle, Inventory reduction, Energy efficiency, Plant location | √√√ | √√√√
Simplification | Number of unit operations, DCS configuration, Raw material quality, Equipment design | √√√√ | √√√√
Moderation (1) [Basic Process] | Conversion conditions, Storage conditions, Dilution, Equipment overdesign | √√√√ | √√√
Moderation (2) [Overall Plant] | Offsite reuse, Advanced waste treatment, Plant location, Beneficial co-disposal | √√√ | √√√
√√√√ = Primary tenet/concepts √√√ = Strongly related tenet/concepts √√ = Some aspects addressed √ = Little relationship |  |  | 
Notes: This table shows strong overlap in concepts of IS and GE. Substitution is a clear example of a concept that overlaps IS and GE. Moderation has a greater relevance to IS than to GE, yet when the process conditions that achieve moderation also improve reaction conversions or reduce process emissions, then there will be a strong GE overlap.

## Slide 15: Similarities between (GE) and (IS)
Benign and less hazardous materials.
Both focus on process changes.
Improving either one often results in improving the other.
Both use a life-cycle approach.
Both are best considered in the initial stages of the design.
Notes: Inherent safer design and green engineering design both encourage the use of benign and less hazardous materials in the process. Examples include the use of environmentally benign and less toxic solvents, fuels, and other raw materials. Both focus on in-process reduction, rather than accepting the hazards/pollution and implementing layers of protection/treatment to control them. The resulting process and product improvements are often beneficial from both environmental and process safety perspectives. Both inherent safer design and green engineering design adopt life-cycle approach, although its use in GE is perhaps more common. When implemented early in design, both GE and IS are the most effective.

## Slide 16: Differences between GE & IS
Focus on a different parts of the product life cycle.
Focus on different aspect of EHS (environmental, health and safety) field and may conflict in application.
Environmental impacts are more numerous than safety impacts.
Notes: Inherently Safety tends to focus only on the chemical processing stage of the life cycle of the chemical product while Green Engineering attempts to minimize environmental impacts throughout the life cycle. GE and IS may conflict. Examples include process simplification versus internal recycle (which in itself adds complexity to a process). The primary concern in process safety is eliminating accidents, both catastrophic failures of process equipment and smaller accidents to workers, as well as minimizing risks to chronic releases to toxic chemicals. On the other hand, the number of environmental impacts that a chemical process or product can have is much larger in comparison.

## Slide 17: Presentation Outline
Introduction to Green Engineering (GE) and Inherent Safety (IS)
  GE definition, concepts, principles, and tools
  IS concepts and tools
  Similarities and differences between GE and IS
Environmentally-Conscious Process Design Methodology
  A hierarchical approach with three “tiers” of impact assessment
  A case study for maleic anhydride (MA) process design
  Early design methods and software tools
  Flowsheet synthesis, assessment, and software tools
  Flowsheet optimization - comparison of process improvement
  Summary of environmentally-conscious design (ECD) methods
Notes: Having covered some introductory concepts of GE in the previous slides, the purpose of this next section is to introduce a hierarchical approach for incorporating environmental impacts in the design of chemical processes. This will be accomplished using a case study design of maleic anhydride production from either benzene or n-butane. Our goal will be to determine which of these routes for production of MA is the least harmful to the environment and the most economical. As we proceed, several topics will be covered, including the hierarchical approach for environmentally-conscious design (ECD) with three “tiers” of environmental impact assessment, a framework for calculating impacts and the models used for this purpose, and key results from the case study.

## Slide 18: Scope of environmental impacts
Pre-Chemical Manufacturing Stages
• Extraction from the environment • Transportation of materials • Refining of raw materials • Storage and transportation • Loading and unloading
Chemical Manufacturing Process
• Chemical reactions • Separation operations • Material storage • Loading and unloading • Material conveyance • Waste treatment processes
Post-Chemical Manufacturing Stages
• Final product manufacture
• Product usage in commerce
• Reuse/recycle
• Treatment/destruction
• Disposal
• Environmental release
• Airborne releases wastewater releases • Solid/hazardous waste • Toxic chemical releases
• Energy consumption • Resource depletion
Environmental/Health Impacts
• Global warming • Ozone layer depletion • Air quality – smog • Acidification • Ecotoxicity
• Human health effects, carcinogenic and non carcinogenic • Resource depletion
Notes: In the design of chemical products and processes, environmental impacts must include all stages in the life cycle. Premaunfacturing impacts include all environmental burdens required to extract materials from the environment, refine, and transport them to the manufacturing facility. Impacts of chemical manufacturing include additional energy consumption and emissions from all activities at the manufacturing facilities. Post chemical manufacturing impacts involve the use of the chemical product, its possible reuse or recycle, treatment, and disposal. Pollutant releases from all of these activities will have impacts on multiple environmental media and and on human health. The main focus of this presentation is the assessment of environmental impacts during the chemical manufacturing stage of the life-cycle.

## Slide 19: Tools of Environmentally-Conscious Chemical Process Design and Analysis
E-CD
Environmental Fate Properties
• databases
• estimation
Chemical Process Properties
• thermodynamics
• reactions
• transport
Chemical Process Models
• simulation
• waste generation and release
Environmental Fate Models
• single compartment
• multi-media
Environmental Impacts Models
• midpoint vs endpoint
• normalization
• valuation
Process Integration
• mass integration
• heat integration
Process Optimization
• multi-objective
• mixed integer
• non-linear
Hierarchical Design
Notes: ECD requires a core set of process design and analysis tools and a framework within which to apply them. The computer-aided tools shown in this slide are used in a sequential fashion as the design progresses, starting with property estimation software and databases. With a known set of chemicals and properties, the process is simulated to obtain a mass and energy balance for the process. Emissions to the environment from process units are estimated using information from the process simulation. The environmental fate of these emitted pollutants is calculated using a multimedia compartment model. Information on emissions and fate are combined to create a set of environmental impact indices which are used to judge and compare competing process designs. After implementing improvement steps through process integration, the improved process flowsheet is optimized using environmental impacts as objectives in the optimization. All of these environmental impact assessment steps are implemented using a hierarchical approach.