## Slide 1: Thermodynamics of electrochemical sourses
Fyodor Malchik

## Slide 2: Energy Levels
An Atom
Energy
E = 0
A Small
Molecule
A Large
Molecule
Filled
States
Empty
States
HOMO
LUMO
Fermi
Level
Vacuum
Level
Chemistry is controlled by the states around the filled/empty transition.
Bulk
Material
Notes: The chemical behaviour of any substance is dictated by its energy levels: their energy, momentum, and density. Even the smallest system, an atom, has an infinite number of energy levels, though only afew are occupied by electrons in its lowest energy condition. As atoms combine to form molecules, the number of states is still infinite but the density of states is spread over a wider range of energy levels. A large molecule is even more complex and finally bulk material has such a high density of states that there seems to be a continuum of states at all energies. Chemistry is controlled by the exchange of electrons around the transition from filled to empty states. In molecules, these are called the LUMO and HOMO states. In a solid they are called the conduction and valence bands. The Fermi level in a solid metal is like the HOMO in a molecule.

## Slide 3: Band Structure
Metal
Core
Bands
Valence
Band
Infinitesimal
spacing
between
filled and
empty states
Small but
non-zero
spacing
between
filled and
empty states
Large
spacing
between
filled and
empty states
Band Gap
Our focus in this course is on metals.
Semiconductor
Insulator
Notes: Vertical direction corresponds to increasing energy. Horizontal direction suggests relative number of states at a given energy. Simplified picture is that the state density is constant. Not true by a long shot, but we use it in simple picture because there are so many states (order of Avogadro’s number) that it is not a bad first scheme.

## Slide 4: Fermi Level
• focus on the electrons near the filled/empty boundary.
E=0 (vacuum level)
EF (Fermi level)
Minimum
energy to
remove
electron
from
sample
• each material’s energy state distribution is unique; different EF.
Metal 1
Metal 2
EF (Fermi level)
• the closer an electron is to the vacuum level, the weaker it is bound to the solid
• or, the more energetic is the electron
Notes: Molecules have chemical bond strengths of a few electron-volts. Bonds are formed by some atoms giving up their electrons and other atoms accepting those electrons. Hence, the important energy states, as far as chemical bond formation is concerned, lie within a few eV of the Homo-Lumo gap. In molecules, that may very well be just the HOMO and the LUMO, but in the solid state, there are many (almost an infinitude) of states near the Fermi level. It is the details of the state density that makes one solid’s chemical behaviour different from another’s.

## Slide 5: Two Conductors in Contact
electron flow
– +
– +
– +
– +
– +
leads to charge separation
Contact potential difference
Fermi level the same throughout sample
Notes: Note that the vacuum level shifts for the two materials. This is because the charge that is transferred establishes a potential that produces the shift in all the states of the sample.

## Slide 6: An Ion in Solution
• ion’s electronic structure: HOMO, LUMO, HOMO-LUMO gap.
Lowest Unoccupied Molecular Orbital
Highest Occupied Molecular Orbital
HOMO-LUMO Gap
“Fermi” level
Notes: Energy levels have breadth because of intramolecular energy states (rotation, vibration) and interactions with the solvent. The Fermi level is in quotes because a Fermi level is actually ionly present for a metal, but the concept is useful here so we use it loosely.

## Slide 7: Metal in an Electrolyte Solution
Fermi levels
are aligned
Charge is transferred to
equilibrate Fermi levels,
producing a charge
separation and a contact
potential difference.
+ –
+ –
+ –
Notes: Charge distribution shown does not have any significance with respect to the energy axis. It is only meant to show that a charge distribution appears at the interface. (More on this tomorrow.)

## Slide 8: Two Electrolyte Solutions
+ –
+ –
+ –
“Fermi” level
A charge separation
arises to align the
“Fermi” level and
produces a potential
at the interface.
Notes: There is even a junction potential produced when the two solutions are of the same substance, but at a different concentration.

## Slide 9: Junction Potentials
• In any circuit there are junction potentials whenever two dissimilar materials come into contact.
• We focus on the metal-solution interface in electrochemistry
Notes: Other interphase junction potentials are always present and they are not negligible. Careful work requires that we account for them. Their contribution is more or less additive and we are able to analyze the interfacial region independently. Just remember that they are there and account for them at the appropriate time.

## Slide 10: Electrochemical Thermodynamics
Every substance has a unique propensity to contribute to a system’s energy. We call this property Chemical Potential.
m
When the substance is a charged particle (such as an electron or an ion) we must include the response of the particle to an electrical field in addition to its Chemical Potential. We call this Electrochemical Potential.
m = m + z F f
These are perhaps the most fundamental measures of thermodynamics.
Notes: Z is the charge on the particle, F is Faraday’s constant, phi is the field under consideration.

## Slide 11: Chemical Potential
Chemical potential (or electrochemical potential if it is charged) is the measure of how all the thermodynamic properties vary when we change the amount of the material present in the system. Formally we can write
Notes: Here we see that the chemical potential describes how the free energy (Gibbs or Helmholtz) and the enthalpy and internal energy all vary with changes in the amount of the material in the system.

## Slide 12: Gibbs Free Energy
The free energy function is the key to assessing the way in which a chemical system will spontaneously evolve.
constant T
constant P
don’t change
shape
don’t stretch it
Notes: If we know the Gibbs function in terms of pressure, temperature and amount of material (T,P, n), then we can, with a variety of partial derivatives, calculate all other thermodynamic properties. If we have the Helmholtz function in terms of (T,V,N) then we have access to all the other parameters also. However, if we only know G in terms of (T,V,n), then we can’t perform the necessary differentials.
There are many ways in which the Gibbs function can change: temperature, pressure, amount of material, surface area, elastic stretch. If we keep everything except material constant, then the changes in the Gibbs function is the result of the changes in the composition of the system.

## Slide 13: Gibbs Function and Work
• Start with the First Law of Thermodynamics and some standard thermodynamic relations. We find
And therefore, the Gibbs function is at the heart of electrochemistry, for it identifies the amount of work we can extract electrically from a system.
Notes: If we start with the First Law of Thermodynamics, we can recall some definitions for heat and work. Under reversible conditions we have the given dq for heat transfer. We also consider for work, either expansion work or electrical work. Substitute these into the First Law equation. Now take the definition for G and, using the definition for enthalpy H, and substitute for internal energy, and cancel terms, we arrive at the important relationship between Gibbs Free Energy and work done in an electrical system.

## Slide 14: Gibbs and the Cell Potential
• Here we can easily see how this Gibbs function relates to a potential.
• By convention, we identify work which is negative with work which is being done by the system on the surroundings. And negative free energy change is identified as defining a spontaneous process.
• Note how a measurement of a cell potential directly calculates the Gibbs free energy change for the process.
Notes: Electrical work is just the amount of charge Q and the potential V through which we move it.
Recall that a process is spontaneous when its change in its Gibbs function is negative. If we choose to associate a positive potential with a spontaneous process, then we need a negative sign in the equation relating ∆G to E.
Must choose a convention for the sign of the cell potential so that it is consistent with these equations and the convention regarding reaction spontaneity and the sign for ∆G.

## Slide 15: Standard Reference States
All thermodynamic measurements are of differences between states; there is no absolute value for any property (exception: entropy does have an absolute measure from theory, but it’s the only one).
In order to quantify thermodynamics, we choose by convention a reference state. Most common choice is called “Standard Ambient Temperature and Pressure (SATP)”.
Temperature = 298 K (25 ˚C)
Pressure = 1 bar (105 Pa)
Concentration = 1 molal (mol of solute/kg of solvent)
BUT…

## Slide 16: Standard Reference States
• atmosphere is a widely used unit of pressure.
• 1 atm = 1.0134 bar
Reference State for Pressure is usually 1 atm
• molality better than molarity
• solvent density is T dependent
• volume changes with T
But…
• volume is easier to measure than mass
• density of water (the most common solvent) is close to 1
The most commonly used reference state is that of 1 M (mol/liter).
Reference states are indicated by superscript ˚
C˚ or P˚
Notes: The use of atmospheres as a unit of pressure is so wide spread and it is so close to the value of 1 bar (1.0134 bar = 1 atm) that the reference state often used is that of 1 atm. The differences are seldom significant.
Concentrations are more reliably measured in molality (amount/mass of solvent) rather than molarity (amount/volume of solvent).
However, for the following reasons: (a) volume is easier to measure than mass and (b) density of water (the most common solvent) is close to 1
The most commonly used reference state is that of 1 M (mol/liter).
Other reference states you may encounter (STP) where T is 273 K and P is 1 atm. Old usage.
Biochemical reference state has T = 37 ˚C (body temperature and C˚(H+ ion) = 10-7 M (closer to human biological conditions).

## Slide 17: Activity
The propensity for a given material to contribute to a reaction is measured by activity, a.
How “active” is this substance in this reaction compared to how it would behave if it were present in its standard state?
• activity scales with concentration or partial pressure.
a  C/C˚ OR a  P/P˚
BUT…
• intermolecular interactions
• deviations from a direct correspondence with pressure or concentration
Notes: Generally speaking, a substance’s activity increases as the amount of that substance available for reaction increases.
However, due to intermolecular interactions (which increase as a substance’s concentration or partial pressure increases) there are deviations from a direction correspondence as pressure and concentration increase. These differences can become very signficant.

## Slide 18: Activity Coefficients
Definition of activity
Activity coefficients close to 1 for dilute solutions and low partial pressures.
• it changes with concentration, temperature, other species, etc. Can be very complex.
Generally, we ignore activity coefficients for educational simplicity, but careful work will require its consideration.
Notes: In the case of pressure, the coefficient used is often called “fugacity” but it is the same thing and behaves in the same way.

## Slide 19: Approximate Activity
• activity is unitless
• activity coefficient is complex over wide ranges of conditions
Since
— activity coefficients are close to 1 for dilute solutions
— reference states for partial pressure and concentration have numerical value of 1
Therefore, we often approximate activity by concentration (M) or partial pressure (atm).
Notes: Activity is unitless since the activity coefficients are unitless and the other term is a ratio.
Other problem is that the activity coefficient can have a very complex behaviour when viewed over a wide range of conditions.

## Slide 20: Solids, Solvents, Liquids
• SOLID: reference is itself
• PURE LIQUID: reference is itself
• SOLVENT: reference is itself
a = 1 for all of these materials
Increase amount of these : reaction goes longer, but not faster.
Notes: The reference state for a solid material is itself.
Same is true for a pure liquid.
A solvent is usually present in a huge excess (compared to the solutes), so it is mostly like a pure liquid.
If you increase the amount of these material in a system, it will not increase the reaction rate but it may increase the duration of a reaction. The point is that the “activity” of the system does not change with amount of these materials, so they are always referenced to themselves.

## Slide 21: Chemical Potential and Activity
How does chemical potential change with activity?
Integration of the expressions for the dependence of amount of material on the Gibbs function, leads to the following relationship:
Notes: Once we have the chemical potential at the reference state, we can readily calculate changes as the activity changes, usually as a result of changes in amount of material, resulting from a chemical reaction.
This will be the foundation by which we analyze any given chemical process to determine its equilibrium position.

## Slide 22: Reaction Quotient
In order to analyze a chemical process mathematically, we form this reaction quotient.
• it always has products in the numerator and reactants in the denominator
• it explicitly requires the activity of each reaction participant.
• each term is raised to the power of its stoichiometric coefficient.
Notes: Watch out for the notation here. I am trying to not confuse you with using “a” for activity and “a” for a stoichiometric coefficient and also not confusing with using gamma for activity coefficient and gamma for stoichiometric coefficient. Hence, the w, x, y, z.
If you write the reaction in a different way, such as write it backwards, or change the stoichiometric coefficients but multiplying by some factor, the quotient changes correspondingly. Write the quotient for the reaction as it appears.

## Slide 23: Simplifying Approximations
• Leave out terms involving solids, pure liquids, and solvents
• Solutes appear as the concentration (in M).
• Gases appear as the partial pressure (in atm).
REACTION QUOTIENT IS UNITLESS.
But its value does depend upon the chosen reference state.
Notes: We leave out of the reaction quotient terms which arising from the participation of solids, liquids, or solvents. This is because their activities are always exactly 1 and do not change the expression. You can remember that they are present in the expression, but just ignored for simplicity of notation.
If we ignore activity coefficients, then activity for solutes and gases are numerically equal to their concentration or partial pressures (since the activity is the ratio of these terms with the number 1). We often write Q with concentration and pressure shown explicitly but remember that we are really writing down activity.
The reaction quotient is unitless because it has only activity in its expression and all activities are unitless. We sometimes write it so that it apparently has units, but this is false.
The numerical value of the reaction quotient does change with selected reference state (M vs. m) or (bar vs. atm) but our simplifying observations make these differences small and we generally ignore them. But careful work will require that you account for this.

## Slide 24: Concentration Dependence
How does Gibbs free energy change with activity (concentration)?
Same dependence as with the chemical potential. We have
When we apply this to a reaction, the reaction quotient comes into to play, giving us
Notes: Q contains all of the activity of terms of the reactants and products, each raised to its stoiochiometric coefficient.

## Slide 25: Equilibrium
When all participants have unit activity (a=1), then Q=1 and ln Q = 0.
This special Q* (the only one for which we achieve this balance) is renamed Keq, the equilibrium constant.
(duh! As designed.)
Reaction proceeds, Q changes, until finally DG=0. The reaction stops. This is equilibrium.
Notes: Use the definition of ∆G and we find that when Q=1, we have ∆G = ∆G˚. This is the way we designed the equation. What is more interesting is to see what happens when ∆G goes to 0. Here is when we reach equilibrium, the various concentrations in the reaction stop changing. The reaction seems to stop. In this case, we obtain a relation between ∆G˚ and the equilibrium constant.
The reaction doesn’t really stop; we simply have reached the situation where the forward and reverse reaction rates are equal. Chemical activity is still ongoing with just as much vigor as before, but it is happening equally in both directions — products are reacting to turn into reactants just as fast as reactants are reacting to turn into products. This is why we call it a dynamic equilibrium, rather than a static equilibrium.

## Slide 26: An Electrochemical Cell
The Weston Cell
Saturated CdSO4
solution
CdSO4 (s)
Hg2SO4 (s)
Hg (l)
Cd(Hg) (l)
—
+
Notes: The Weston Cell was invented by Edward Weston in 1893. It was been used for a very long time as an excellent voltage reference source, producing 1.0180 V at 25 ˚C. The output is stable and reproducible. Note that it has some environmental drawbacks, however, with all the mercury and cadmium in it.

## Slide 27: Weston Cell Reactions
Here are the two reactions that are occurring. In the left-hand cell we find
Cd(Hg) ® Cd2+(aq) + 2e–
• Cd is being oxidized (its oxidation number is going from 0 to +2)
In the right-hand cell we find
Hg2SO4(s) + 2e– ® 2 Hg(l) + SO42–(aq)
• Hg is being reduced (its oxidation number is going from +1 to 0)
The overall reaction is the sum of these two reactions
Cd(Hg) + Hg2SO4(s) ® 2 Hg(l) + Cd2+(aq) + SO42–(aq)
This reaction occurs spontaneously as written. Its free energy change ∆G is therefore –ive and its cell potential E is +ive.
Notes: If you can’t remember how to assign oxidation numbers, go to any first year chemistry textbook to refresh your memory.
Remember to make sure your reactions are multiplied by appropriate coefficients so that the electrons cancel between the two reactions.
When a reaction is written down and its cell potential or Gibbs free energy are calculated, the reaction proceeds spontaneously as written if ∆G is negative and E is positive. If the opposite is the case, then the reaction needs to be written in reverse to represent the spontaneous process.

## Slide 28: Cell Notation
A shorthand cell notation has been developed for convenience. The Weston cell is written as
Cd(12.5% Hg amalgam) | CdSO4(aq, sat) | Hg2SO4 (s) | Hg(l)
• write components in sequence
• separate phases with a single vertical line “|”
• a salt bridge or membrane is represented by a double vertical line “||”
• included a specification of the species concentration
• note that the solid CdSO4 is necessary to maintain a saturated solution, but it does not participate directly in the reaction so it is not included in the cell definition
Notes: Get a first year chemistry textbook and try a few cell notation examples.

## Slide 29: Electrode Convention
The electrode at which oxidation is occurring is called the anode.
The electrode at which reduction is occurring is called the cathode.
• write the anode on the left and the cathode on the right.
• a cell operating spontaneously in this configuration is said to have a positive total cell potential.
• when connecting a voltmeter, connect the positive terminal to the positive electrode. If it reads a positive potential, you have correctly identified all the terminals. If you read a negative potential, then you have misidentified the reactions in the cells, and you have hooked it up backwards. Reverse your assignment of anode and cathode.
• in a galvanic cell the cathode is +ive
• in an electrolytic cell the cathode is –ive.
Notes: These definitions hold true even if the cells is running as a galvanic cell (producing electricity) or a electrolytic cell (being charged, or depositing material).
The pneumonic that oxidation and anode but start with a vowel, while reduction and cathode both start with a consonant.
The polarity of each half-cell changes with how the cell is being run. If it is galvanic, then at the cathode reduction is spontaneously occurring. This means that the reaction is consuming electrons and this is why there are fewer electrons than normal and why the electrode is positively charged with respect to the other terminal. In a electrolytic cell, the reaction is still one of reduction, but this time we are forcing it to occur by adding in more electrons than would be there normally. This induces the reaction to occur and explains why it is negatively charged.

## Slide 30: Daniell Cell
CuSO4 (aq)
ZnSO4 (aq)
Cu metal
Zn metal
salt bridge
Cathode (reduction)
+ive
Anode (oxidation)
–ive
Zn(s) ® Zn2+(aq) + 2e–
Cu2+(aq) + 2e– ® Cu(s)
Notes: This is another important cell from the early days of electrochemistry. Large banks of these cells were used to power early telegraph systems.
Here we find that the reaction proceeds spontaneously such that Zn metal dissolves and copper metal plates out on their respective electrodes. Note also that the two sides are connected by a salt bridge. This permits the passage of ions, but prevents the two solutions from mixing directly.

## Slide 31: Salt Bridge
What is the role of the salt bridge?
Carefully merge two solutions. Make CuSO4 more dense than ZnSO4. Sheath Cu electrode in glass.
Liquid-liquid interface
Daniell Cell without salt bridge
Salt bridge makes cell
construction and
operation easier.
Pack tube with a viscous, aqueous
solution of KCl or KNO3. The
viscosity prevents mixing with
the electrolytes. The ions permit
exchange of charge. The chosen
ions have similar mobility to
minimize junction potentials.
Notes: It is possible to fabricate a Daniell cell without a salt bridge. If you make the two electrolyte solutions so that one is of a higher density (make it more concentrated, for instance. (1) Put the ZnSO4 in the beaker. (2) Use a funnel to introduce the CuSO4 to the bottom layer without mixing with the ZnSO4 (pour it in slowly). Place a glass sheath around the Cu electrode and insert it down into the bottom layer. Add the Zn electrode and it works! Yes. There is reaction at the interfacial region between the two solutions, but diffusion soon limits reactivity and it becomes a chemically quiet zone. Reaction proceeds nicely - until something jostles the beaker and mixes the two solutions.
A salt bridge simplifies the task of cell construction and operation. By packing a glass tube with a viscous, aqueous ionic solution, we can allow charge transport without allowing the two solutions to mix with each other. Often the solution is an agar jell with KCl or KNO3. The K+, Cl–, and NO3– ions have similar mobilities and migrate in opposite directions with similar velocities. This minimizes the appearance of junction potentials in the bridge.

## Slide 32: Flow of Charge
How does charge flow in a cell?
Zn2+
NO3–
Zn
Cu2+
NO3–
Cu
V
Cl–
K+
e–
e–
If concentrations are 1M, then the cell is at standard conditions and the measured potential is +1.10 V.
+
–
Notes: Place the Zn electrode into its electrolyte solution. The Fermi level of electronic charge in the two solutions is different (and dependent upon the concentration of Zn2+ in the solution). There is an exchange of charge across the interface interconverting Zn metal and Zn2+ ions. This process proceeds until a junction potential is produced that offsets the chemical potential driving the process forward. A dynamic equilibrium results, wherein the forward and reverse processes balance and a static potential results and the Fermi level in the system is now equilibrated. This happens in a few nanoseconds.
A similar process occurs when we place the Cu electrode in the Cu solution. After equilibration, its Fermi level, while flat throughout the system, is not the same as that in the Zn system. It will be lower than the Zn Fermi level.
If we now introduce the salt bridge (let’s say it is made of KCl), some K+ ions will flow into the Cu half-cell and some Cl– ions will flow into the Zn half-cell. This is an attempt to even out the Fermi level in the entire system, now that it is connected. Zn will surrender electrons to produce Zn2+ in an effort to maintain electrical neutrality. Similarly Cu2+ will consume electrons (found in its Cu electrode, of course) making that electrode more positive while the Zn electrode is more negative. Finally a potential develops between the two electrodes that balances the chemical potential driving the two processes. A dynamic equilibrium results.
If now we connect the two electrodes, a current will flow, whereby electrons from the Zn flow into the copper electrode. If the resistance of this connection is low, the current can be very high. If we use a voltmeter with a high impedance (MW), then the current will be very small. A measurement of the potential difference will be accurate in this case.
Any current we allow to flow, will tend to discharge the potential difference. To much current flowing will lead to an inaccurate measurement.

## Slide 33: Electrolytic Cell
What about running the cell in reverse?
Zn2+
NO3–
Zn
Cu2+
NO3–
Cu
DC V
Cl–
K+
e–
e–
• apply an external voltage of opposite polarity.
• magnitude must exceed the +1.10 V that the cell produces on its own.
• Cu electrode now dissolves and Zn now plates out on its electrode.
+
–
Notes: If we apply a voltage in such a manner as to oppose the natural potential of the cell, we can force the reactions to proceed in reverse. Now we start to steal electrons away from Cu atoms and drive the ions into solution, while we force electrons into the Zn electrode and insist that the Zn2+ ions pick them up, plating out the Zn on the electrode.
A galvanic cell is one which is allowed operate in its natural direction. An electrolytic cell is one which is being operated in reverse.
A galvanic cell produces a potential to drive an external load. An electrolytic cell is one which consumes external electricity.
A galvanic cell is like a battery or a fuel cell.
An electrolytic cell is often used to process materials electrochemically.
Note that the electrode polarity changes between galvanic and electrolytic. The identity of the electrode also changes. However, the one constant is the definition for reduction and oxidation. Oxidation is Loss; Reduction is Gain. “OIL RIG”.

## Slide 34: Half-Cell Potentials
It is best to think of a cell’s operation in terms of the two reactions taking place at the two electrodes separately.
• can understand each half-cell reaction in isolation
• makes classifying and tabulating data easier
Cd(Hg)
CdSO4 solution
Hg
1.018 V
Anode Potential Difference
Cathode Potential DIfference
Notes: If we think about half-cell reactions, we can study each process in isolation. Then, the concepts we arrive at when considering the Cu/Cu2+ electrode can be applied to all other cells in which it is participating. The alternative is to study and catalogue the information from every combination of cell possible. Such a task would excessively complicate and obfuscate the field.
The potential of an electron is constant as it passes through the various conducting phases of the cell (the electrode, the electrolyte solution). It changes its potential at phase boundaries over distances of a few molecular diameters. This fact nicely divides the problem into two halves and validates this concept of half-cell potentials.
Consider the Weston cell. The electron falls in potential as it moves from the cathode to the anode. At each phase boundary it gains energy and is the source of the electromotive force delivered by the cell.

## Slide 35: Standard Reduction Potentials
Convention: We discuss half-cell reactions from a point of view of their being reduction processes.
Weston Cell Cathode:
Hg2SO4(s) + 2e– ® 2 Hg(l) + SO42–(aq)
This is a reduction and is the half-cell process we consider.
Weston Cell Anode:
Cd(Hg) ® Cd2+(aq) + 2e–
This is an oxidation. We must consider the reverse process in our convention.
Cd2+(aq) + 2e– ® Cd(Hg)
Notes: To make discussion of the matter easier, we agree to tabulate and analyze half-cells when they are behaving as reduction processes. When a process is occurring as an oxidation, we simply will reverse our analysis and data.
The Weston Cell has already been broken into the anode and cathode processes. The anode, however, needs to be reversed in our considerations.
This convention of selecting cathodes is somewhat arbitrary. We could have just as easily selected the oxidation processes as the convention. Indeed, many decades ago, this was the convention. If you scan through textbooks from the 1960’s and earlier you will find tables of standard oxidation potentials. The convention of that time agreed to standardize on reduction potentials and this is now the absolute standard in all electrochemical work.

## Slide 36: So What Is The Half-Cell E˚?
To complete each Nernst equation we need to know the potential difference between each electrode and the solution. This we cannot measure directly.
Cd(Hg)
CdSO4 solution
Hg
?
?
?
Solution: Adopt an arbitrary reference electrode.
Notes: WE do not have a means of measuring the potential difference between the electrode and the solution. To do so would require the interposition of another piece of metal to connect to our measuring device and we would have another interface which would alter the potential again. Our experiments really say nothing about the potential inside the solution phase. We only measure the differences between the two electrodes. Any possible intermediate phase is viable. There are some theoretical arguments and some indirect results from measurements of interfacial tension and interfacial capacitance. But these have not been adopted as a direct measure of interfacial potential difference.
The solution is to adopt an arbitrary, but extremely useful convention.

## Slide 37: Standard as a Reference
Once chosen, this reference cell is employed as one half-cell with all other cells. Since its potential is assigned the value of 0.000 V, all of the potential difference measured experimentally is attributed to the other, test electrode.
Since we are cataloguing reduction potentials, the cells are formed by connecting the Standard Hydrogen Electrode (SHE) as the anode and the other half-cell as the cathode.
Consider:
Pt | H2 (1.00 atm) | H+ (1.00 M) || Cu2+ (1.00 M) | Cu
Measured potential = +0.340 V
Since the activity of all components in the Cu cell are standard, +0.340 V is the STANDARD REDUCTION POTENTIAL of the Cu2+/Cu couple.
Notes: Our convention dictates that we hookup the cell so that the positive input terminal to the voltmeter is connected to our test cell and the negative terminal to the SHE. This is how to hook up a system when the test cell is a cathode. Any potential we measure will be its cathodic or reduction potential. If the cell potential is measured to be positive, then the process under test really was functioning as a reduction. If the measured potential is negative, then the test cell was operating as an oxidation. Rather than catalogue only positive potentials, but distinguishing between those which are reductions and those which are oxidations, we catalogue only reductions, but those with negative potentials are actual operating in reverser when paired with the SHE.

## Slide 38: By Contrast…
Consider the Zn2+/Zn half-cell.
Pt | H2 (1.00 atm) | H+ (1.00 M) || Zn2+ (1.00 M) | Zn
Measured Cell Potential = -0.7626 V
This is the Standard Reduction Potential for this couple.
• negative potential means it really is being oxidized
• convention accounts for that with the negative sign when written as a reduction.
• will make for easier use of tables.
Notes: The fact that it is negative means that in reality in our test cell, Zn was being oxidized. The negative sign accounts for that and is considered to be an easier way to report than to amek everything positive but some oxidations and some reductions.

## Slide 39: Standard Potential Tables
All of the equilibrium electrochemical data is cast in Standard Reduction Potential tables.
F2 + 2e– ® 2F– +2.87
Co3+ + e– ® Co2+ +1.81
Au+ + e– ® Au +1.69
Ce4+ + e– ® Ce3+ +1.61
Br2 + 2e– ® 2Br– +1.09
Ag+ + e– ® Ag +0.80
Cu2+ + 2e– ® Cu +0.34
AgCl + e– ® Ag + Cl– +0.22
Sn4+ + 2e– ® Sn2+ +0.15
2H+ + 2e– ® H2 0.0000
Pb2+ + 2e– ® Pb -0.13
Sn2+ + 2e– ® Sn -0.14
In3+ + 3e– ® In -0.34
Fe2+ + 2e– ® Fe -0.44
Zn2+ + 2e– ® Zn -0.76
V2+ + 2e– ® V -1.19
Cs+ + e– ® Cs -2.92
Li+ + e– ® Li -3.05
Notes: These are all for aqueous environments, which is implied by the use of the SHE as the reference state. We often leave implied that all ions are present in aqueous solution and solids or gases or liquids are implied, depending upon the form at the standard state of 25 ˚C and 1 atm pressure.
Note the Br2 is a liquid under standard conditions. AgCl is a solid. Compare that reduction with that for Ag+. The same thing is happening (Ag+ is picking up an electron) but note the difference in potential.
These tables are cast here in the order known as the “electrochemical series”. We start with the most strongly oxidizing reaction and go down to the most weakly oxidizing reaction.
Other tables that are useful, tabulate the data alphabetically or grouped according to other elemental classifications. If you are looking for a specific reaction, such an alphabetic table is most useful. The electrochemical series is most useful when comparing two reactions to see which will induce oxidation or reduction in the other.

## Slide 40: Using the Tables
• choose one reaction for reduction
• choose another for oxidation
F2 + 2e– ® 2F– +2.87
Co3+ + e– ® Co2+ +1.81
Au+ + e– ® Au +1.69
Ce4+ + e– ® Ce3+ +1.61
Br2 + 2e– ® 2Br– +1.09
Ag+ + e– ® Ag +0.80
Cu2+ + 2e– ® Cu +0.34
AgCl + e– ® Ag + Cl– +0.22
Sn4+ + 2e– ® Sn2+ +0.15
Overall Reaction:
2Au+ + Cu ® Cu 2+ + 2Au
Au+ + e– ® Au
Cu ® Cu2+ + 2e–
Cell potential E:
E = +1.69 - 0.34 = +1.35 V
Notes: Every cell reaction consists of a reduction reaction and an oxidation reaction. Hence, every cell must be constructed to employ one reaction written as it appears in the table and another reaction written opposite to how it appears in the table.
The one we select as an oxidation, we write backwards.
We need to balance the number of electrons; multiply the Au equation by 2. Add the equations to obtain the total reaction equation.
Here we see that a cell constructed using a Au and a Cu electrode and solutions of Au(I) and Cu(II) ions, when at unit activity (1.00 M) has a potential of +1.35 V. This indicates that indeed the Au electrode is the cathode for the reduction process is occurring there. Conversely, the copper electrode is the anode and oxidation is occurring there.

## Slide 41: Calculating Cell Potential
Because we tabulate reduction potentials, the cell potential is calculated (from those tabulated numbers) as
Ecell = Ecathode - Eanode
The minus sign is present only because we are using reduction potential tables and, by definition, an anode is where oxidation occurs.
Notes: This equation, cathode - anode, has the form it does because of the convention we have chosen. The numbers that go in here are the ones from the table. Don’t switch the anodic potential around and then use this equation. The negative sign is there precisely so that will be done.

## Slide 42: Example
Fe2+ + 2e– ® Fe -0.44
V2+ + 2e– ® V -1.19
To get a final positive cell potential, the more negative half-reaction (V) must act as the anode.
Fe2+ + V ® Fe + V2+
Ecell = -0.44 - (-1.19) = +0.75 V
Sn2+ + 2e– ® Sn -0.14
Ag+ + e– ® Ag +0.80
More negative potential reaction is the anode.
Multiply the Ag reaction by 2, but don’t modify the cell potential.
2 Ag+ + Sn ® 2 Ag + Sn2+
Ecell = +0.80 - (-0.14) = +0.94 V
Notes: Take two reactions. Let the more negative (least positive) reaction be that for the anode. That means that its direction will be reversed. Balance the number of electrons but scaling the reactions appropriately, but DO NOT modify their cell potentials. The cell potential is a “per charge” quantity, so it does not change with the amount of material making the change. This is in contrast to all other thermodynamic properties such as free energy, enthalpy, or entropy, which are scaled by the same amount as the reaction.

## Slide 43: Oxidative Strength
Consider a substance on the left of one of these equations. It will react as a reactant with something below it and on the right hand side.
• higher in the table means more likely to act in a reducing manner.
• when something is reduced, it induces oxidation in something else.
• it is an oxidizing agent or an oxidant.
• F2 is a stronger oxidant than Ag+.
• Cu2+ is a weaker oxidant than Ce4+.
F2 + 2e– ® 2F– +2.87
Co3+ + e– ® Co2+ +1.81
Au+ + e– ® Au +1.69
Ce4+ + e– ® Ce3+ +1.61
Br2 + 2e– ® 2Br– +1.09
Ag+ + e– ® Ag +0.80
Cu2+ + 2e– ® Cu +0.34
AgCl + e– ® Ag + Cl– +0.22
Sn4+ + 2e– ® Sn2+ +0.15

## Slide 44: Reductive Strength
Substances on the right hand side of the equations will react so as to be oxidized.
• LOWER in the table means a greater tendency to be oxidized.
• when oxidized, it induces reduction in something else. It is a reducing agent or reductant.
• Ag is a stronger reductant than Au.
• Co2+ is a weaker reductant than Sn2+
F2 + 2e– ® 2F– +2.87
Co3+ + e– ® Co2+ +1.81
Au+ + e– ® Au +1.69
Ce4+ + e– ® Ce3+ +1.61
Br2 + 2e– ® 2Br– +1.09
Ag+ + e– ® Ag +0.80
Cu2+ + 2e– ® Cu +0.34
AgCl + e– ® Ag + Cl– +0.22
Sn4+ + 2e– ® Sn2+ +0.15
Notes: Reducing agents are on the right hand side of the equations in a table of reduction potentials. The stronger reducing agents are found lower in the table (and on the right hand side.) The stronger oxidizing agents are found higher in the table on the left hand side.